## Slide 1: Gears – Angular Velocity Ratio
Source: Kinematic analysis and synthesis of mechanisms by Mallik, Ghosh and Dittrich

## Slide 2: Constant Angular Velocity Ratio
Source: Kinematic analysis and synthesis of mechanisms by Mallik, Ghosh and Dittrich
Can be achieved using a belt pulley system:
Angular velocity ratio is same as the inverse ratio of the diameters

## Slide 3: Involute Profile
Source: Kinematic analysis and synthesis of mechanisms by Mallik, Ghosh and Dittrich
The curves on the shaded area are the involute profiles.
Obtained by tracing the point Q on the shaded flanges attached to pulleys 1 and 2.

## Slide 4: Involute Profile
Source: Kinematic analysis and synthesis of mechanisms by Mallik, Ghosh and Dittrich
Path of contact is always the line AB.
Thus the situation is same as the crossed belt and pulley system
Constant angular velocity ratio is maintained.

## Slide 5: Gear Mesh Design – Spur and Helical
Useful quantities:

## Slide 6: Gear Mesh Design – Spur and Helical
Criteria:
Load, speed, reliability, life (N), overload (Ko), design factor (nd)
Apriori Decisions:
Pressure angle (f), Helix angle (y)
Addendum (a), Deddendum (d), root fillet radius (rF)
Gear Ratio (mG), Numer of teeth (Np, NG)
Quality Number (Qv)
Design Decisions:
Module (m), Face width (b)
Pinion Material, core hardness, case hardness
Gear Material core hardness, case hardness

## Slide 7: Design Steps
Choose a module:
Check for Pinion bending and wear (pitting)
    Choose material and a core hardness
    Calculate face width to satisfy safety factor and standardize (ensure 3p m ≤ b ≤ 5p m)
    Compute AGMA factors of safety SF and SH
    If not satisfactory modify module and repeat until the design is satisfactory
Check for Gear bending and wear (pitting)
    Choose material and a core hardness
    Compute AGMA factors of safety SF and SH
    If not satisfactory modify module and repeat until the design is satisfactory

## Slide 8: Gear Force Analysis

## Slide 9: AGMA Equations for Bending (SI Units)
AGMA Stress Equation for Bending:
Condition of support | Face width |  |  | 
 | Up to 50 mm | Up to 150 mm | Up to 225 mm | Up to 400 mm
Accurate mounting, low bearing clearances, minimum elastic deflection, precision gears | 1.3 | 1.4 | 1.5 | 1.8
Less rigid mounting, less accurate gears, contact across full face | 1.6 | 1.7 | 1.8 | 2.0
Accuracy and mounting such that less than full-face contact exists | Over 2.0 |  |  | 

## Slide 10: AGMA Equations for Bending (SI Units)
AGMA Strength Equation for Bending:

## Slide 11: AGMA Equations for Pitting (SI Units)
AGMA Stress Equation for Contact (pitting):

## Slide 12: AGMA Equations for Pitting (SI Units)
AGMA Strength Equation for Pitting: