## Slide 1: Rolling Contact Bearings
Rolling contact bearings: Load is transferred through elements in rolling contact.
Also called anti-friction bearing due to its low friction characteristics.
Advantage: Lower price, low maintenance, ease of operation
Application: Extensively used
Ball bearings
Source: RAS Bearings and Industrial Components

## Slide 2: Types of Rolling Contact Bearings
Rolling bearings Types:
Ball Bearings: Rolling elements are spherical balls
Roller Bearings: Rolling elements are rollers (cylindrical or straight, tapered, spherical)
Ball bearing
Source: indiantradebird.com
Straight roller
globalcpec.com
Tapered roller bearing
Source: globalcpec.com
Spherical roller bearing
Source: SKF
Ball Bearings: Can take radial and axial thrust load
Straight Roller Bearings: Larger load capacity than ball bearings
            Zero misalignment required
            Can not take axial thrust

## Slide 3: Types of Rolling Contact Bearings
Ball bearing
indiantradebird.com
Straight roller
globalcpec.com
Tapered roller bearing
Source: globalcpec.com
Spherical roller bearing
Source: SKF
Ball Bearings: Lower load capacity, Can take radial and axial thrust load
Straight Roller Bearings: Larger load capacity than ball bearings, Zero misalignment required
            Can not take axial thrust
Tapered Roller Bearings: High load capacity, Some misalignment permitted,
            Load: Radial, axial thrust and combined radial and thrust
Tapered Roller Bearings: Heavy load capacity, Large misalignment permitted,
            Increases contact area with increased load

## Slide 4: Types of Rolling Contact Bearings
Types of Ball Bearings:
Types of Roller Bearings

## Slide 5: Bearing Components
Ball bearing
Source: encyclopedia2.thefreedictionary.com

## Slide 6: Bearing Assembly
Bearing Assembly
Source: Aggregates and Mining Today

## Slide 7: Bearing Life
Load on Bearings: Fluctuation contact stress (on ball or roller, and the races)
Failure Scenario: Fatigue (for proper lubrication, mounting, sealing, temperature and
            Dust control)
Measure of Life: (1) Number of revolutions of inner ring with outer fixed before fatigue.
            (2) Hours of operation at constant angular speed before fatigue
Fatigue Criterion: Pitting or spalling of an area 0.01 square inch (6.5 sq. mm)
This is for constant reliability R

## Slide 8: Bearing Selection
Rated Load and Life: Provided in Manufacturer’s Catalog.
              Compare with desired load and life
From Catalog select a bearing with rating FR or higher.
This is for constant reliability R
For 90 % reliability (R=0.9): (FR, , LR ) are called (C10, , L1o )